QE-GIPAW User Manual
Author: Davide Ceresoli <davide.ceresoli@materials.ox.ac.uk>
Last revision: 04/15/11

QE-GIPAW is an improved version of the GIPAW code distributed in Quantum-Espresso. QE-GIPAW is distributed as a stand-alone package that must be compiled against Quantum-Espresso.

# Features
- Periodic and isolated systems
- Norm-conserving and ultrasoft pseudopotentials
- Parallelization over k-points (pools) and g-vectors
- Automatic checkpoint and restart
- Magnetic susceptibility
- NMR chemical shielding tensors
- Electric Field Gradients (EFG)
- EPR g-tensor
- Hyperfine couplings
# Authors
- D. Ceresoli	bare susceptibility, hyperfine core
- A. P. Seitsonen and U. Gerstmann	GIPAW reconstruction
- E. Kucukbenli	ultrasoft and PAW pseudopotentials
- S. de Gironcoli	restart and bug fixes
For further information and to report bugs, please contact:
- Davide Ceresoli	davide.ceresoli@materials.ox.ac.uk, dceresoli@gmail.com
- Emine Kucukbenli	kucukben@sissa.it
# Build instructions
1. Configure and compile quantum-Espresso in the usual way. The supported version are 4.3, 4.3a, 4.3b and the current SVN version.
2. Download QE-GIPAW from tarball or from SVN. QE-GIPAW can be downloaded and built outside the Quantum-Espresso folder:
   From tarball:
   tar zxfv qe-gipaw-4.3.tar.gz
   cd qe-gipaw-4.3
   From SVN:
   svn checkout svn://cvs.qe-forge.org/scmrepos/svn/qe-gipaw/trunk qe-gipaw
   cd qe-gipaw
3. Build QE-GIPAW:
   ./configure --with-qe-source=<quantum espresso folder containing make.sys>
   (for example: ./configure –with-qe-source=$HOME/Codes/espresso-4.3)
   make
QE-GIPAW will be built according to the options and libraries specified in make.sys and the gipaw.x executable will be placed in the bin folder.
# Quick start
To calculate NMR/EPR parameters you need:
1. pseudopotentials containing the GIPAW reconstruction (look into folder pseudo)
2. run pw.x to perform the SCF calculation
3. run gipaw.x to calculate parameters (look into folder examples for NMR shielding, EFG, EPR g-tensor and hyperfine couplings)
# Input file description
The input file consists on only one namelist &inputgipaw:
Variable: job	type: character	default: 'nmr'
Description: select calculation to perform. The possible values are:
'f-sum'	check the f-sum rule
'nmr'	compute the magnetic suscept. and NMR chemical shifts
'efg'	compute the electric field gradients at the nuclei
'g_tensor'	compute the EPR g-tensor
'hyperfine'	compute the hyperfine couplings

Variable: prefix	type: character	default 'pwscf'
Description: prefix of files saved by program pw.x

Variable: tmp_dir	type: character	default: './scratch/'
Description: temporary directory where pw.x files resides

Variable: max_seconds	type: real	default: 107	units: s Description: max wall time clock before writing the checkpoint and terminate

Variable: conv_threshold	type: real	default: 10–14	units: Rydberg2
Description: convergence threshold for the diagonalization and for the Green's function solver

Variable: isolve	type: integer	default: 0
Description: diagonalization method (Davidson = 0, CG = 1)

Variable: q_gipaw	type: real	default: 0.01	units: bohr-1
Description: the small wave-vector for linear response

Variable: iverbosity	type: integer	default: 0
Description: if iverbosity > 0 print debug information in output

Variable: filcurr	character	default: ''
Description: file name for the induced current

Variable: filfield	type: character	default: ''
Description: file name for the induced current

Variable: use_nmr_macroscopic_shape	type: logical	default: .false.
Description: correct the chemical shift by taking into account the macroscopic shape of the sample

Variable: nmr_macroscopic_shape(3,3)	type: real	default: 2/3
Description: shape tensor for the macroscopic shape correction

Variable: spline_ps	type: logical	default: .true.
Description: interpolate pseudopotentials with cubic splines

Variable: q_efg(1..ntyp)	type: real	default: 0.0	units: 10-30 m2 = 0.01 barn
Description: for each atomic specie, the nuclear quadrupole

Variable: hfi_output_unit	type: character	default: 'MHz'
Description: units for hyperfine couplings in output. The possible values are: 'MHz', 'mT', 'G', 'Gauss', '10e-4cm-1'

Variable: hfi_nuclear_g_factor(1..ntyp)	type: real	default: 0.0
Description: for each atomic specie, the nuclear g-factor

Obsolete/development variables (do not use):
radial_integral_splines
hfi_via_reconstruction_only
hfi_extrapolation_npoints
pawproj(1..ntyp)
read_recon_in_paratec_fmt
file_reconstruction(1..ntyp)
# Limitations
Symmetry operations that do not map cartesian axes are not allowed (i.e. 120° rotations). If you have a triclinc cell, remove all symmetries (nosym = .true.). In the special case of an hexagonal cell, you can use ibrav = 0 and orient the cell like in the quartz example. The keyword CELL_PARAMETERS cubic prevents PW to detect 120° rotations.
# Resources
Websites: http://qe-forge.org/projects/qe-gipaw, http://www.gipaw.net
NMR periodic table: http://www.pascal-man.com/periodic-table/periodictable.html
Tutorials: http://www.gipaw.net/work_zurich09.html, http://sites.google.com/site/cecamspectra2010/program (day 2)
# References
1. C. J. Pickard and F. Mauri, Phys. Rev. B 63, 245101 (2001)
2. J. R. Yates, C. J. Pickard and F. Mauri, Phys. Rev. B 76, 024401 (2007)
3. C. J. Pickard and F. Mauri, Phys. Rev. Lett. 63, 245101 (2001)